## Slide 1: Enabling the Adoption of Data-Centric Systems: Hardware/Software Support for Processing-Using-Memory Architectures
Geraldo F. Oliveira geraldofojunior@gmail.com
https://geraldofojunior.github.io/
Memory & Storage Summit 2024 − 07 December 2024
Notes: Hi, I’m Geraldo, a PhD Student under the supervision of professor Multu at ETH Zurich and I’ll be talking about our work DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks.
[NEXT]

## Slide 2: Brief Self Introduction
Geraldo F. Oliveira
  Researcher @ SAFARI Research Group since November 2017
  Soon, I will defend my PhD thesis, advised by Onur Mutlu
  https://geraldofojunior.github.io/
  geraldofojunior@gmail.com (best way to reach me)
  https://safari.ethz.ch
Research in:
  Computer architecture, computer systems, hardware security
  Memory and storage systems
  Hardware security, safety, predictability
  Fault tolerance
  Hardware/software cooperation
  …

## Slide 3: Data Movement Bottlenecks (1/2)
DRAM
CPU
CPU
CPU
L2
L1
L3
L2
L1
L2
L1
L2
L1
CPU
Data Movement
Data movement bottlenecks happen because of:
  Not enough data locality → ineffective use of the cache hierarchy
  Not enough memory bandwidth
  - High average memory access time
Off-Chip Link
4
Notes: Data movement has become an key bottleneck for modern systems.
[CLICK] Intuitively, it does become an issue because of at least three different reasons:
[CLICK] because infective use of the cache hierarchy in applications with poor data locality
[CLICK] because the main memory cannot provide enough memory bandwidth
[CLICK] or because the application or system cannot tolerate the high average memory access time cause by frequent accesses to main memory
[NEXT].

## Slide 4: Huge Demand for Performance & Efficiency
https://www.youtube.com/watch?v=x2-qB0J7KHw
~4 orders of magnitude increase in memory requirement in just two years!

## Slide 5
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Data Movement Overwhelms Modern Machines

## Slide 6
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]
> 90% of the total system energy
is spent on memory in large ML models
Data Movement Overwhelms Modern Accelerators

## Slide 7: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 8: Data Movement Bottlenecks (2/2)
  - Abundant DRAM bandwidth
  - Shorter average memory access time
  - Abundant per-array parallelism
DRAM
CPU
CPU
CPU
L2
L1
L3
L2
L1
L2
L1
L2
L1
CPU
Compute-Centric Architecture
Off-Chip Link
DRAM
CPU
CPU
CPU
L1
L1
L1
L1
CPU
Off-Chip Link
Memory-Centric Architecture
Processing-in-Memory (PIM)
…
Notes: High-performance systems have evolved to include mechanisms that aim to alleviate data movement’s impact on system performance and energy consumption, such as deep cache hierarchies and aggressive prefetchers. We refer to such mechanisms as compute-centric.
However, such mechanisms not only come with significant hardware cost and complexity, but they also often fail to hide the latency and energy costs of accessing DRAM in many modern and emerging applications.
[CLICK]
[CLICK] One promising technique that aims to alleviate the data movement bottleneck in modern and emerging applications are memory-centric architectures.
[CLICK] In such architectures, the cost of data movement is reduced by placing computation capability close to memory.
[CLICK] Near-Data processing, or NDP, is a good example of a memory-centric architecture.
[CLICK] In a NDP design, the logic close to memory has access to data that in main memory with higher memory bandwidth and shorter latency than the CPU has in existing systems.
[NEXT]

## Slide 9: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 10: Processing-in-Memory: Overview
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 11: Processing-in-Memory: Landscape of Real Systems (I)
Processing-in-Memory architectures are now commercially available
Alibaba HB-PNM
Hybrid bonding with logic
for recommendation systems
SK hynix AiM
Near-DRAM-bank processing
for neural networks
Notes: Even though processing-in-memory is an old idea, it is just recently that the first PIM architectures have become commercially available.
[CLICK] For example, the UPMEM PIM system, provided by a company of same name, proposes a PIM system with near-DRAM-banking processing elements for general purpose computing
[CLICK] Another example is Samsung’s HBM-PIM system which targets accelerating neural network inference.
[NEXT]

## Slide 12: Processing-in-Memory: Landscape of Real Systems (II)
Processing-in-Memory architectures are now commercially available
UPMEM
Near-DRAM-bank processing
for general-purpose computing
Samsung HBM-PIM
Near-DRAM-bank processing
for neural networks
Notes: Even though processing-in-memory is an old idea, it is just recently that the first PIM architectures have become commercially available.
[CLICK] For example, the UPMEM PIM system, provided by a company of same name, proposes a PIM system with near-DRAM-banking processing elements for general purpose computing
[CLICK] Another example is Samsung’s HBM-PIM system which targets accelerating neural network inference.
[NEXT]

## Slide 13: Processing-in-Memory: Landscape of Real Systems (II)
Processing-in-Memory architectures are now commercially available
Samsung HBM-PIM
Near-DRAM-bank processing
for neural networks
UPMEM
Near-DRAM-bank processing
for general-purpose computing
Notes: In this presentation, we will focus on the UPMEM PIM system
[NEXT]

## Slide 14: Processing-in-Memory: The UPMEM Architecture
UPMEM: Near-DRAM-bank processing for general-purpose computing
Integration of UPMEM PIM in a system follows an accelerator model
Notes: The UPMEM PIM system is composed of a collection of simple in-order multi-threaded cores that have access to a low latency DRAM bank and an SRAM-based scratchpad memory.
[CLICK] The UPMEM PIM chip is integrated in a system following a loosely coupled accelerator model
[NEXT]

## Slide 15: The Programmability Barrier: Overview
  Programming the UPMEM-based system requires:
1
Splitting input data and computation across PIM chips
2
Transferring input data from main memory to PIM chips
3
Manually handling caching in PIM’s scratchpad memory
4
Transferring output data from PIM chips to main memory
Programming a general-purpose PIM architecture leads to non-trivial effort → requires knowledge of the underlying hardware and manual fine-grained data movement handling
1
2
3
4
1
2
3
4
Notes: In order to program the UPMEM system, the programmer needs to perform four main operations.
[CLICK] First, it needs to split input data across PIM chips
[CLICK] Second, it needs to transfer input data from main memory to PIM chips
[CLICK] Third, it needs to manually handle caching inside the PIM’s scratchpad memory
[CLICK] and fourth, it needs to transfer output data from PIM chips to main memory
[NEXT]

## Slide 16: The Programmability Barrier: Summary
Align data | Collect parameters | Distribute parameters | Launch computation | Collect results | Manage scratchpad | Orchestrate computation | Just write my kernel
Programmer’s Tasks:
Goal:
static void vector_addition(T *bufferB, T *bufferA, int l_size){
for (unsigned int i = 0; i < l_size; i++){
bufferB[i] += bufferA[i];
}
}
Programming the UPMEM system leads to non-trivial effort → requires knowledge of the underlying hardware and manual fine-grained data movement handling
Problem
Notes: We conclude that programming the UPMEM system leads to non-trivial effort by the programmer since it requires knowledge of the underlying hardware and manual data movement handling
[NEXT[

## Slide 17: Our Goal
To ease programmability for the UPMEM system, allowing a programmer to write efficient PIM-friendly code
without the need to explicitly manage hardware resources
Goal
Notes: Therefore, our goal in this work is to ease programmability for the UPMEM system, allowing the programmer to write PIM-friendly code efficiently.
[NEXT]

## Slide 18: SimplePIM: A Software Framework for Productive and Efficient Processing in Memory
Jinfan Chen, Juan Gómez-Luna, Izzat El Hajj, Yuxin Guo, and Onur Mutlu, "SimplePIM: A Software Framework for Productive and Efficient Processing in Memory" Proceedings of the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023. [Slides (pptx) (pdf)] [SimplePIM Source Code]

## Slide 19: SimplePIM Programming Framework: Overview
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
1
  Management interface → Metadata for PIM-resident arrays
2
  Communication interface → Abstractions for host-PIM and PIM-PIM communication
3
  Processing interface → Iterators (map, reduce, zip) to implement workloads
Notes: [CLICK] Our software framework, SimplePIM, leverages the massive memory bandwidth and parallelism offered by PIM hardware to operate on arrays of arbitrary size and dimensions. SimplePIM offers three key interfaces to support PIM systems like UPMEM.
[CLICK] The management interface stores metadata for the PIM-resident arrays, which can be accessed by the programmer and other parts of SimplePIM as needed.
[CLICK] The communication interface provides abstractions for both Host-PIM and PIM-PIM communication patterns.
These patterns are similar to communication patterns in other distributed frameworks such as MPI [71], which makes it easier for SimplePIM to be adopted.
[CLICK] The processing interface leverages PIM’s high memory bandwidth and parallelism to execute map, reduce, and zip iterators on PIM arrays.
Programmers can combine these iterators to implement many widely-used workloads ranging from simple vector addition to complex machine learning model training.
[CLICK] Let’s check each one of these interfaces next
[NEXT]

## Slide 20: Evaluation Results: Evaluation Methodology
Evaluated system
  UPMEM PIM system with 2,432 PIM cores with 159 GB of PIM DRAM
Real-world Benchmarks
  Vector addition
  Reduction
  Histogram
  K-Means
  Linear regression
  Logistic regression
Comparison to hand-optimized codes in terms of programming productivity and performance

## Slide 21: Evaluation Results: Productive Improvement (I)
Example: Hand-optimized histogram with UPMEM SDK
... // Initialize global variables and functions for histogram
int main_kernel() {
if (tasklet_id == 0)
mem_reset(); // Reset the heap
... // Initialize variables and the histogram
T *input_buff_A = (T*)mem_alloc(2048); // Allocate buffer in scratchpad memory
for (unsigned int byte_index = base_tasklet; byte_index < input_size; byte_index += stride) {
// Boundary checking
uint32_t l_size_bytes = (byte_index + 2048 >= input_size) ? (input_size - byte_index) : 2048;
// Load scratchpad with a DRAM block
mram_read((const __mram_ptr void*)(mram_base_addr_A + byte_index), input_buff_A, l_size_bytes);
// Histogram calculation
histogram(hist, bins, input_buff_A, l_size_bytes/sizeof(uint32_t));
}
...
barrier_wait(&my_barrier); // Barrier to synchronize PIM threads
... // Merging histograms from different tasklets into one histo_dpu
// Write result from scratchpad to DRAM
if (tasklet_id == 0)
if (bins * sizeof(uint32_t) <= 2048)
mram_write(histo_dpu, (__mram_ptr void*)mram_base_addr_histo, bins * sizeof(uint32_t));
else
for (unsigned int offset = 0; offset < ((bins * sizeof(uint32_t)) >> 11); offset++) {
mram_write(histo_dpu + (offset << 9), (__mram_ptr void*)(mram_base_addr_histo +
(offset << 11)), 2048);
}
return 0;
}

## Slide 22: Evaluation Results: Productive Improvement (II)
Example: SimplePIM histogram
// Programmer-defined functions in the file "histo_filepath"
void init_func (uint32_t size, void* ptr) {
char* casted_value_ptr = (char*) ptr;
for (int i = 0; i < size; i++)
casted_value_ptr[i] = 0;
}
void acc_func (void* dest, void* src) {
*(uint32_t*)dest += *(uint32_t*)src;
}
void map_to_val_func (void* input, void* output, uint32_t* key) {
uint32_t d = *((uint32_t*)input);
*(uint32_t*)output = 1;
*key = d * bins >> 12;
}
// Host side handle creation and iterator call
handle_t* handle = simple_pim_create_handle("histo_filepath", REDUCE, NULL, 0);
// Transfer (scatter) data to PIM, register as "t1"
simple_pim_array_scatter("t1", src, bins, sizeof(T), management);
// Run histogram on "t1" and produce "t2"
simple_pim_array_red("t1", "t2", sizeof(T), bins, handle, management);
// Run histogram on "t1" and produce "t2"
simple_pim_array_red("t1", "t2", sizeof(T), bins, handle, management);
// Transfer (scatter) data to PIM, register as "t1"
simple_pim_array_scatter("t1", src, bins, sizeof(T), management);
// Host side handle creation and iterator call
handle_t* handle = simple_pim_create_handle("histo_filepath", REDUCE, NULL, 0);

## Slide 23: Evaluation Results: Productive Improvement (III)
Lines of code (LoC) reduction
 | SimplePIM | Hand-optimized | LoC Reduction
Reduction | 14 | 83 | 5.93×
Vector Addition | 14 | 82 | 5.86×
Histogram | 21 | 114 | 5.43×
Linear Regression | 48 | 157 | 3.27×
Logistic Regression | 59 | 176 | 2.98×
K-Means | 68 | 206 | 3.03×
SimplePIM reduces the number of lines of effective code by a factor of 2.98× to 5.93×

## Slide 24: Evaluation Results: Weak Scaling Analysis
SimplePIM achieves comparable performance for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression,
and k-means by 10%-37%

## Slide 25: Evaluation Results: Strong Scaling Analysis
SimplePIM scales better than hand-optimized implementations for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression, and k-means by 15%-43%

## Slide 26: Source Code
https://github.com/CMU-SAFARI/SimplePIM

## Slide 27: SimplePIM: A Software Framework for Productive and Efficient Processing in Memory
Jinfan Chen, Juan Gómez-Luna, Izzat El Hajj, Yuxin Guo, and Onur Mutlu, "SimplePIM: A Software Framework for Productive and Efficient Processing in Memory" Proceedings of the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023. [Slides (pptx) (pdf)] [SimplePIM Source Code]

## Slide 28: DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures
Geraldo F. Oliveira, Alain Kohli, David Novo, Juan Gómez-Luna, Onur Mutlu ”DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures,” arXiv:2310.10168 [cs.AR] 2nd Place ACM Student Research Competition at the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023.

## Slide 29: DaPPA: Key Idea & Overview
Leverage an intuitive data-parallel pattern-based interface for PIM programming
Key Idea
DaPPA , a Data-Parallel PIM Architecture that automatically distributes input and gathers output data, handles memory management, and parallelizes work across PIM cores
1
Data-Parallel Pattern APIs
2
Dataflow Programming Interface
3
Dynamic Template-Based Compilation
  DaPPA is composed of three main components:
Notes: The key idea behind DaPPA is to use an intuitive data-parallel pattern Based programming interface for PIM
[CLICK] DaPPA uses such an interface to automatically distribute and gather data across PIM chips, handle memory management and to parallelism computation across PIM cores
[CLICK] DaPPA is composed of three main components.
[CLICK] A collection of data-parallel pattern APIs
[CLICK] A dataflow programming interface
[CLICK] and a dynamic template-based compilation
[NEXT]

## Slide 30: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: Let’s see how DaPPA can be used to implement a simple dot product operation in the UPMEM system
[NEXT]

## Slide 31: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: First, the programmer chooses suitable data parallel patterns to represent the computation. In this case, a map and reduce patterns
[NEXT]

## Slide 32: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: Second, the user creates two pipeline stages in C++ to implement the computation. Note that there is no hardware specific code required here.
[NEXT]

## Slide 33: DaPPA: Putting All Together
Example of DaPPA’s implementation of a
vector dot product operation
Notes: Finally, DaPPA takes the C++-based pipeline, and dynamically compiles and executes each stage in the UPMEM system.
[NEXT]

## Slide 34: Evaluation: Methodology Overview
Evaluation Setup
  Host CPU: 2-socket Intel® Xeon Silver 4110 CPU
  PIM Cores: 20 UPMEM PIM DIMMs (160 GB PIM memory)
  2560 DPUs in total
Workloads: 6 workloads from the PrIM benchmark suite
  Vector addition (VA); Select (SEL); Unique (UNI); Reduce (RED); General matrix-vector multiply (GEMV); Histogram small (HST-S)
Metrics
  End-to-end execution time (average of 10 runs)
  Programming complexity (in lines of code)
Notes: We evaluate DaPPA using a real UPMEM system with more than 2000 PIM cores
[CLICK] We use six workloads from the PrIM benchmark suite
[CLICK] We compare DaPPA’s performance and programming complexity against the hand-tuned PrIM workloads
[NEXT]

## Slide 35: Evaluation: Performance Analysis
Chart: Normalized Performance
| VA | SEL | UNI | RED | GEMV | HST-S | GMEAN
PrIM | 1 | 1 | 1 | 1 | 1 | 1 | 1
DaPPA | 1.125 | 10 | 10 | 1.1 | 0.93333 | 0.93333 | 2.1
Large performance improvement due to parallel data transfers & host+PIM collaborative exec.
Notes: In this plot, we show DaPPA’s performance normalized to the hand-tuned PrIM implementations.
[CLICK] We observe a large performance improvement for some workloads, due to DAPPA usage of parallel data transfers and collaborative host and PIM execution
[NEXT[

## Slide 36: Evaluation: Performance Analysis
Chart: Normalized Performance
| VA | SEL | UNI | RED | GEMV | HST-S | GMEAN
PrIM | 1 | 1 | 1 | 1 | 1 | 1 | 1
DaPPA | 1.125 | 10 | 10 | 1.1 | 0.93333 | 0.93333 | 2.1
2.1x
DaPPA significantly improves end-to-end performance
compared to hand-tuned implementations
Notes: Overall, DAPPA provides 2.1x the performance of hand-tuned code.
[NEXT]

## Slide 37: Evaluation: Programming Complexity Analysis
DaPPA significantly reduces programming complexity
by abstracting hardware components
Chart: Lines of Code (LOC)
| VA | SEL | UNI | RED | GEMV | HST-S | GMEAN
PrIM | 78 | 120 | 155 | 123 | 180 | 113 | 123.9683
DaPPA | 6 | 6 | 6 | 6 | 9 | 8 | 6.7348
Reduction | 0.92308 | 0.95 | 0.96129 | 0.95122 | 0.95 | 0.9292 | 0.94404
94.4%
Notes: Next, we evaluate programming complexity measured in lines of code.
[CLICK] On average, DaPPA reduces the required lines of code by 94% compared to PrIM.
[NEXT]

## Slide 38: Evaluation: Comparison to State-of-the-Art
SimplePIM [Chen+, PACT’23]: a framework that uses (1) iterator functions and (2) primitives for communication to aid PIM programmability Compared to SimplePIM, DaPPA provides three key benefits
  Higher abstraction level → The programmer does not need to manually specify communication patterns used during computation
  Support for more parallel patterns → DaPPA supports two more parallel primitives (window and group), and allows the mixing of parallel patterns
  Further execution optimizations → DaPPA allows using idle host resources for collaborative execution
DaPPA improves state-of-the-art frameworks for PIM programmability
Notes: We briefly compared DaPPA to a previously proposed framework for PIM programmability called SimplePIM.
Compared to SimplePIM, DaPPA provides
[CLICK] A higher abstraction level, where the user does not need to manually specific communication across PIM cores as in SIMPLE PIM; two more parallel patterns, and further optimizations as colloborative PIM+host execution.
[CLICK] We conclude that DaPPA improves the state-of-the-art in PIM programmability
[NEXT]

## Slide 39: DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures
Geraldo F. Oliveira, Alain Kohli, David Novo, Juan Gómez-Luna, Onur Mutlu ”DaPPA: A Data-Parallel Framework for Processing-in-Memory Architectures,” arXiv:2310.10168 [cs.AR] 2nd Place ACM Student Research Competition at the 32nd International Conference on Parallel Architectures and Compilation Techniques (PACT), Vienna, Austria, October 2023.

## Slide 40: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 41: Background: DRAM Hierarchical Organization
local sense amplifier
local row decoder
bitline
wordline
DRAM subarray
(e.g., 65,536 rows)
DRAM mat
(e.g., 512 rows & columns)
Notes: DRAM chips are hierarchically organized.
[CLICK] On the bottom level, we have a DRAM mat, which is a 2D array of DRAM cells
[CLICK] Rows in a DRAM mat share a wordline,
[CLICK] and columns share a bitline
[CLICK] Columns are connected to a set of local sense amplifiers
[CLICK] and rows are connected to a local row decoder
[CLICK] Multiple DRAM mats constitute a DRAM subarray
[NEXT]

## Slide 42: Background: DRAM Hierarchical Organization
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Notes: The many mats in a DRAM subarray are indexed using a global row decoder, which propagates the target row address across all mats using the global wordline
[CLICK] To move data outside a mat, a DRAM subarray uses a global sense amplifier,
[CLICK] and to move data outside a DRAM subarray, a DRAM chip uses the I/O logic interface
[NEXT]

## Slide 43: Background: DRAM Operation – Row Access (ACTIVATE)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Notes: To access data, the memory controller executes two main operations.
[CLICK] To access a DRAM row, the memory controller issues an ACTIVATE command to DRAM. On receiving an ACT, the global and local row decoder assess the wordline of the target row, connecting the DRAM cells to the bitlines
[CLICK] Then, the sense amplifier senses the perturbation caused in the bitline, amplifying and latching the data from the DRAM cells
[NEXT]

## Slide 44: Background: DRAM Operation – Column Access (READ)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
column
to memory channel
global wordline
Notes: Then, the memory controller issues a read command to read a column of data from the previously latched DRAM row.
[CLICK] The read command moves the target DRAM column from the local sense amplifiers to the global sense amplifier and finally to the memory channel via the I/O interface
[NEXT]

## Slide 45: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
← src
← dst
Notes: The operating principles of DRAM can be used to implement bulk-bitwise operations inside DRAM. For example, RowClone implements in-DRAM row copy operation by issuing back-to-back ACTIVATE commands to DRAM
[CLICK] The first activate copies the source row into the local sense amplifier
[NEXT]

## Slide 46: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy improves performance & energy: 1046 ns, 3.6 uJ → 90 ns, 0.04 nJ
← src
← dst
Notes: The second activate connects the destination row to the local sense amplifier.
[CLICK] which allows the previously-latched source row to be written back to the destination row.
[NEXT]

## Slide 47: Background: In-DRAM Majority Operations
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority is performed by simultaneously activating three DRAM rows
← src3
← src2
← src1
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 48: Background: In-DRAM Majority Operations
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority reduces energy: 137.9 nJ/KB → 3.2 nJ/KB
← src3
← src2
← src1
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 49: Background: PUD in Commodity Off-the-Shelf (COTS) DRAM
Commodity off-the-shelf DRAM chips can perform bulk bitwise operations without hardware modifications
https://arxiv.org/pdf/2402.18736.pdf
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 50: PUD in COTS DRAM: Summary of Results
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 51: PUD in COTS DRAM: Experimental Setup
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 52: PUD in COTS DRAM: Tested DRAM Chips
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 53: PUD in COTS DRAM: Testing Methodology
Carefully sweep:
  Row addresses: Row A and Row B
  Timing parameters: Between ACT → PRE and PRE → ACT
ACT row A
PRE
ACT row B
neighboring subarrays
subarray X
subarray Y
row A
row B
ACT
DRAM bank
ACT
shared sense amplifiers
Notes: In this study, we focus on two neighboring subarrays, here denoted as Subarray X and Subarray Y, which share a common component, sense amplifiers
[CLICK] We perform our experiment using the following command sequence: Activate Row A, which is in the subarray X, Precharge, and Activate Row B
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 54: PUD in COTS DRAM: Conclusion
We experimentally demonstrate that commercial off-the-shelf (COTS) DRAM chips can perform:
  Functionally-complete Boolean NOT, NAND, and NOR
  Up to 16-input AND, NAND, OR, and NOR operations
We characterize the success rate of these operations on 256 COTS DDR4 chips from two major manufacturers
We highlight two key results:
  We can perform NOT and {2, 4, 8, 16}-input AND, NAND, OR, and NOR operations on COTS DRAM chips with very high success rates (>94%)
  Data pattern and temperature only slightly affect the reliability of these operations
We believe these empirical results demonstrate
the promising potential of using DRAM as a computation substrate

## Slide 55: More on: RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013.

## Slide 56: More on: In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 57: More on: Ambit
Vivek Seshadri, Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017.

## Slide 58: More on: Functionally-Complete DRAM
Ismail Emir Yuksel, Yahya Can Tugrul, Ataberk Olgun, F. Nisa Bostanci, A. Giray Yaglikci, Geraldo F. Oliveira, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024.

## Slide 59: Processing-in-Memory: Challenges
  To fully support PIM systems, we need to develop:
1
Workload characterization methodologies and benchmark suites targeting PIM architectures
2
Frameworks that can facilitate the implementation of complex operations and algorithms using PIM primitives
3
Compiler support and compiler optimizations targeting PIM architectures
4
Operating system support for PIM-aware virtual memory, memory management, data allocation and mapping
5
Efficient data coherence and consistency mechanisms
  The lack of tools and system support for PIM architectures limit the adoption of PIM system

## Slide 60: Processing-in-Memory: In This Talk
3
Compiler support and compiler optimizations targeting PIM architectures
4
Operating system support for PIM-aware virtual memory, memory management, data allocation and mapping
  To fully support PIM systems, we need to develop:
1
Workload characterization methodologies and benchmark suites targeting PIM architectures
5
Efficient data coherence and consistency mechanisms
  The lack of tools and system support for PIM architectures limit the adoption of PIM system
2
Frameworks that can facilitate the implementation of complex operations and algorithms using PIM primitives

## Slide 61: Frameworks for PIM: SIMDRAM
Geraldo F. Oliveira, Nastaran Hajinazar, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021.

## Slide 62: Our Goal
Design a PUM framework that
(1) Efficiently implements complex operations
(2) Flexibility supports new PUM operations
(3) Minimally changes the DRAM architecture
Goal
Notes: Accordingly, [CLICK] our goal is to design a processing using memory framework that,
[CLICK] Efficiently implements complex operations
[CLICK] Provides the flexibility to support new desired operations
[CLICK] Minimally changes the DRAM architecture

## Slide 63: SIMDRAM Framework: PUM Substrate & Key Ideas
SIMDRAM framework is built around a DRAM substrate that enables two techniques:
(1) Vertical data layout
4-bit element size
Row Decoder
most significant bit (MSB)
least significant bit (LSB)
A
B
Cout
Cin
MAJ
(2) Majority-based computation
Pros compared to the conventional horizontal layout:
Implicit shift operation
Massive parallelism
Cout= AB + ACin + BCin
Pros compared to AND/OR/NOT-based computation:
Higher performance
Lower energy consumption
Notes: We build the SIMDRAM
framework around a DRAM substrate that enables two
key techniques: first, [CLICK] vertical data layout in DRAM
[CLICK] Prior works show that employing a vertical layout for the data in DRAM, eliminates the need for adding extra logic in DRAM to implement bit-shift operation which is essential for many complex operations.
[CLICK] Employing vertical data layout provides SIMDRAM with two key benefits:
[CLICK] implicit shift operation
[CLICK] and massive parallelism, wherein each DRAM column operates as a SIMD lane
[CLICK] The second key technique used in SIMDRAM’s substrate is majority based computation. As opposed to using basic logic operations such as AND/OR/NOT to implement in-DRAM computation, SIMDRAM uses [CLICK] logically complete set of majority (MAJ) and NOT operations to implement in-DRAM computation.
Doing so [CLICK] enables SIMDRAM to achieve [CLICK] higher performance, [CLICK] higher throughput, and [CLICK] lower energy consumption compared to using basic logical operations for in-DRAM computation.

## Slide 64: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
Notes: SIMDRAM is an end-to-end framework that provides the user with
the ability to implement an arbitrary operation in DRAM
The framework is composed of three main steps which are illustrated in this picture.
[CLICK] It takes as user input input the AND/OR/NOT representation of a desired operation.
[CLICK] Step 1 builds an efficient MAJ/NOT representation of a given desired operation from its AND/OR/NOT-based implementation. Specifically, this step takes as input a desired
operation and uses logic optimization to minimize the number of logic primitives (and, therefore, the computation latency) required to perform the operation.
[CLICK] The second step allocates DRAM rows to the operation’s inputs and outputs and generates the required sequence of DRAM commands to execute the desired operation.
[CLICK] This step’s output is a μProgram, i.e., the optimized sequence of DRAM commands that is stored in main memory and will be used to execute the operation at runtime. The uProgram
[CLICK] is stored in main memory and will be used to execute the operation at runtime
[CLICK] and a new SIMDRAM instruction called bbop is created as an interface to the uProgram, and then added to the CPU ISA
[CLICK] The third step executes the μProgram to perform the operation. SIMDRAM uses a control unit in the memory controller that transparently issues the sequence of commands to DRAM, as dictated by the μProgram. Once the μProgram is complete, the result of the operation is held in DRAM.
[NEXT]

## Slide 65: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 66: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 67: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← tmp
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
A
Sum
MAJ
Cout
MAJ
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 68: Background: Bulk Bitwise Arithmetic Operations
← A
← tmp
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 69: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 70: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Processing-Using-DRAM architectures (e.g., SIMDRAM) are very-wide (e.g., 65,536 wide) bit-serial SIMD engines
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 71: Evaluation: Methodology Overview (I)
Simulator: gem5
Baselines:
  A multi-core CPU (Intel Skylake)
  A high-end GPU (NVidia Titan V)
  Ambit: a state-of-the-art in-memory computing mechanism
Evaluated SIMDRAM configurations (all using a DDR4 device):
  1-bank: SIMDRAM exploits 65’536 SIMD lanes (an 8 kB row buffer)
  4-banks: SIMDRAM exploits 262’144 SIMD lanes
  16-banks: SIMDRAM exploits 1’048’576 SIMD lanes
Notes: [CLICK] We implement SIMDRAM using gem5 simulator
[CLICK] We compare SIMDRAM against three baselines
[CLICK] a multi-core CPU
[CLICK] a high-end GPU
[CLICK] and, Ambit, an state-of-the-art in-DRAM computing mechanism
[CLICK] We evaluate three different configurations of SIMDRAM
[CLICK] 1-bank configuration, where a single DRAM bank is extended to enable SIMDRAM computation. This enables SIMDRAM to execute operations over 64K SIMD lanes
[CLICK] We also evaluate SIMDRAM with four in-DRAM computation enabled banks
[CLICK] And 16 in-DRAM computation enabled banks.
[NEXT]

## Slide 72: Evaluation: Methodology Overview (II)
16 complex in-DRAM operations:
  Absolute - Predication
  Addition/Subtraction - ReLU
  BitCount - AND-/OR-/XOR-Red
  Equality/ Greater/Greater Equal - Division/Multiplication
7 real-world applications
  BitWeaving (databases) - LeNET (Neural Networks)
  TPC-H (databases) - VGG-13/VGG-16 (NNs)
  kNN (machine learning) - brightness (graphics)
Notes: [CLICK] To demonstrate its generality, we evaluate SIMDRAM using
[CLICK] 16 complex in-DRAM operations
And [CLICK] 7 commonly-used real-world applications from various domains
[NEXT]

## Slide 73: Evaluation: Throughput Analysis
Chart: Average Normalized Throughput (GOPS/s) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 5.5 | 0.36 | 1.98
SIMDRAM - 4 Banks | 22 | 1.5 | 7.9
SIMDRAM - 16 Banks | 88.01 | 5.82 | 31.61
SIMDRAM significantly outperforms
all state-of-the-art baselines for a wide range of operations
Average normalized throughput across all 16 SIMDRAM operations
Notes: First, we compare the throughput across all 16 SIMDRAM operations, normalized to the three baselines.
[CLICK] Here, the X axis shows each one of the three baselines we evaluated, and the Y axis shows the average normalized throughput in GigaOPerations per second. We make the following observations.
[CLICK] First, SIMDRAM with a single bank provides 5.5x the throughput of the baseline CPU
[CLICK] This value increases to 22x the throughput of the baseline CPU using four DRAM banks
[CLICK] and to 88x the throughput of the CPU using 16 DRAM banks.
[CLICK] Second, SIMDRAM with a single bank is not enough to outperform the throughput of the GPU.
[CLICK] However, with four DRAM banks, SIMDRAM provides 1.5x the throughput of the GPU
[CLICK] which scales to 5.8x when using 16 DRAM banks.
[CLICK] Third, compared to Ambit, SIMDRAM 1 bank provides 2x Ambit's throughput of Ambit.
[CLICK] While SIMDRAM 4 banks provides 7.9x
[CLICK] And SIMDRAM 16 banks provides 31.6x the throughput of Ambit.
[CLICK] We conclude that SIMDRAM can largely outperform all three state-of-the-art baselines for a wide range of operations
[NEXT]

## Slide 74: Evaluation: Energy Analysis
Average normalized energy efficiency across all 16 SIMDRAM operations
Chart: Average Energy Efficiency (GOPS/s/Watt) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 257 | 31 | 2.6
SIMDRAM - 4 Banks | 257 | 31 | 2.6
SIMDRAM - 16 Banks | 257 | 31 | 2.6
SIMDRAM is more energy-efficient than
all state-of-the-art baselines for a wide range of operations
Notes: Second, we compare the energy efficiency across all 16 SIMDRAM operations, normalized to the three baselines.
[CLICK] Here, the X axis shows each one of the three baselines we evaluated, and the Y axis shows the average normalized energy efficiency in Throughput per Watt. We make the following observations.
[CLICK] SIMDRAM provides 257x the energy efficiency of the CPU baseline,
[CLICK] 31x the energy efficiency of the high-end GPU
[CLICK] And 2.6x the energy efficiency of Ambit
[CLICK] We conclude that SIMDRAM is more energy efficient than all state-of-the-art baselines
[NEXT]

## Slide 75: Evaluation: Real-World Applications
Chart: Average Speedup -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 3 | 0.30612 | 2.5
SIMDRAM - 4 Banks | 8.7 | 0.88776 | 7.25
SIMDRAM - 16 Banks | 21 | 2.1429 | 17.5
SIMDRAM effectively and efficiently accelerates
many commonly-used real-world applications
Average speedup across 7 real-world applications
Notes: Third, we compare the speedup across all 7 real-world applications,
[CLICK] First, SIMDRAM with a single bank provides 3x speedup compared to the baseline CPU
[CLICK] which scales to 8.7x using four DRAM banks and
[CLICK] 21x using all 16 SIMDRAM-capable banks
[CLICK] Second, SIMDRAM with a single bank and
[CLICK] with four banks is not enough to outperform the GPU.
[CLICK] However, by using all 16 SIMDRAM-capable banks, SIMDRAM provides an average speedup of 2.1x compared to the GPU
CLICK] Third, SIMDRAM with a single bank provides 2.5x speedup compared to Ambit
[CLICK] which scales to 7.3x using four DRAM banks and
[CLICK] 17.5x using all 16 SIMDRAM-capable banks
[CLICK] We conclude that SIMDRAM can effectively and efficiently accelerate many commonly used real-world applications.

## Slide 76: SIMDRAM & HBM-PIM: TransPIM [Zhou+, HPCA'22]
Key Idea:
to combine PUD and PND to achieve high efficiency and throughput transformer inference
point-wise vector operations are performed in DRAM cells
the vector reduction and part of softmax
are offloaded to a
near-DRAM bank
accelerator
TransPIM is 22.1x to 114.9x faster than a GPU (Nvidia RTX 2080Ti) for RoBERTa, Pegasus, and GPT-2 models
Zhou, Minxuan, et al. ”TransPIM: A Memory-based Acceleration via
Software-Hardware Co-Design for Transformer," in HPCA, 2022
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 77: Frameworks for PIM: pLUTo
João Dinis Ferreira, Gabriel Falcao, Juan Gómez-Luna, Mohammed Alser, Lois Orosa, Mohammad Sadrosadati, Jeremie S. Kim, Geraldo F. Oliveira, Taha Shahroodi, Anant Nori, and Onur Mutlu, "pLUTo: Enabling Massively Parallel Computation in DRAM via Lookup Tables" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022.

## Slide 78
?
input
output
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
x
LUT[x]
x
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 79
input
LUT[x]
output
x
x
ALU
x
input
f(x)
output
x
pLUTo: Key Idea
Replace computation with memory accesses
→ pLUTo LUT Query operation
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 80
row buffer
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
0
1
2
3
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 81
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
0
1
2
3
row buffer
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 82
0
0
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 83
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
match logic
Accessing
the 2nd (1) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 84
match logic
Accessing
the 2nd (1) prime number?
input
vector
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
input
vector
row buffer
pLUTo
row sweep
0 = 1 ?
1
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 85
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
?
𝘅
input
vector
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 86
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
𝘅
input
vector
input
vector
row buffer
Accessing
the 1st (0) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 87
input
vector
Accessing
the 1st (0) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
row buffer
𝘅
0
pLUTo
row sweep
0 = 0 ?
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 88
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 89
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 90
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
input
vector
?
✓
𝘅
input
vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 91
Accessing
the 4th (3) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
?
✓
𝘅
𝘅
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 92
0
1
2
3
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
7 | 7 | 7 | 7
𝘅
✓
𝘅
𝘅
3 | 2 | 3 | -
7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 93
pLUTo Designs: Tradeoff Space
Chart: 
| Performance | Energy Efficiency | Area Efficiency
BSA | 8 | 8 | 5
GSA | 4 | 4 | 10
GMC | 10 | 10 | 3
v
Performance
Area Efficiency
Energy Efficiency
Gated Sense Amplifier
Buffered Sense Amplifier
Gated Memory Cell
pLUTo designs cover a broad design space and provide different performance, energy, and area efficiency

## Slide 94
Methodology: Experimental Setup
Baselines
  CPU (Intel® Xeon Gold 5118)
  GPU (NVIDIA® GeForce RTX 3080 Ti)
  Processing-near-Memory (PnM)
pLUTo
  In-house simulator, open-sourced
  https://github.com/CMU-SAFARI/pLUTo
We evaluate:
  Performance
  Energy consumption
  Area overhead
  Circuit-level reliability and correctness
  …

## Slide 95
Methodology: Workloads
7 real-world workloads (not well supported by prior work)
  CRC-8/16/32
  Salsa20
  VMPC
  Image Binarization
  Color Grading
4 synthetic workloads (supported by prior work)
  Vector Addition
  Vector Point-Wise Multiplication
  Row-Level Bitwise Logic Operations
  Bit Counting

## Slide 96
Average speedup across 7 real-world workloads
Performance
Chart: Average Speedup
| CPU | GPU | PnM
pLUTo-GSA | 357 | 0.6 | 9.2
pLUTo-BSA | 713 | 1.2 | 18.3
pLUTo-GMC | 1413 | 2.3 | 36.2
pLUTo significantly outperforms CPU, GPU and PnM baselines

## Slide 97
Average energy consumption across 7 real-world workloads
Energy Consumption
Chart: Average Energy Salving
| CPU | GPU | PnM
pLUTo-GSA | 1361.7035 | 28.9664
pLUTo-BSA | 1854.9695 | 39.4592
pLUTo-GMC | 3071.3751 | 65.3348
pLUTo significantly reduces energy consumption compared to processor-centric architectures for various workloads

## Slide 98: Processing-in-Memory: In This Talk
2
Frameworks that can facilitate the implementation of complex operations and algorithms using PIM primitives
  To fully support PIM systems, we need to develop:
1
Workload characterization methodologies and benchmark suites targeting PIM architectures
5
Efficient data coherence and consistency mechanisms
  The lack of tools and system support for PIM architectures limit the adoption of PIM system
3
Compiler support and compiler optimizations targeting PIM architectures
4
Operating system support for PIM-aware virtual memory, memory management, data allocation and mapping

## Slide 99: Compilers & Systems for PUM: MIMDRAM
Geraldo F. Oliveira, Ataberk Olgun, Abdullah Giray Yaglikci, F. Nisa Bostanci, Juan Gomez-Luna, Saugata Ghose, and Onur Mutlu, "MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Processing" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), April 2024.

## Slide 100: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Notes: Processing-using-DRAM architectures suffers from three main limitations due to the rigid and large DRAM access granularity
[CLICK] First, they suffer from SIMD underutilization
[CLICK] Second, they suffer from a limited computation support
[CLICK] Third, they have a challenging programming model
Let me elaborate on each limitation next
[NEXT]

## Slide 101: MIMDRAM: Key Idea (I)
DRAM’s hierarchical organization can enable fine-grained access
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
global sense amplifier
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 102: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 103: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 104: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 105: MIMDRAM: Key Idea (III)
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 106: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 columns
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 107: MIMDRAM: Overview
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Notes: Based on that, we proposed MIMDRAM, a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and low programming effort
[CLICK] MIMDRAM constitutes of hardware and
[CLICK] software components, which I will elaborate on next.
[NEXT]

## Slide 108: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting with our new compiler support for PUD applications
[NEXT]

## Slide 109: MIMDRAM: Modifications to DRAM Chip
inter-mat
interconnect
row decoder
global wordline
mat range
mat selector
isolation transistors
row decoder latch
IO interface
global
sense amplifier
helper FFs
Notes: This data path allows us to move data across adjacent DRAM mats
[NEXT]

## Slide 110: MIMDRAM: Control Unit Design
The control unit schedules and orchestrates the execution of multiple PUD operations transparently
Notes: The goal of MIMDRAM’s control unit, implemented at the memory controller, is to schedule and orchestrate the execution of multiple PUD operations transparently from the user. I highlight three main components of our control unit.
[CLICK] First, the mat scheduler is responsible for identifying which PUD operations can be dispatched based on the current mat utilization
[CLICK] Second, the mat scoreboard keeps track of the current utilized mats
[CLICK] and the uProgram processing engines dispatch DRAM access for a given running PUD operation
[NEXT]

## Slide 111: MIMDRAM: More in the Paper
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
https://arxiv.org/pdf/2402.19080.pdf
https://github.com/CMU-SAFARI/MIMDRAM
Notes: Starting with our new compiler support for PUD applications
[NEXT]

## Slide 112: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting with our new compiler support for PUD applications
[NEXT]

## Slide 113: MIMDRAM: Compiler Support
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 114: MIMDRAM: System Support
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Notes: I will brief discuss our data allocation & alignment routine
[NEXT]

## Slide 115: MIMDRAM: Data Allocation & Alignment
MIMDRAM’s memory allocator uses a pool of huge pages and reversed-engineered DRAM interleaving information for PUD memory objects
Notes: MIMDRAM requires data from PUD operations to map to the target DRAM mats correctly.
To allow the memory allocator to influence the physical data location for PUD operations, we implement a new memory allocator that leverages huge pages and reversed-engineered DRAM inter;eaving information for PUD memory objects.

## Slide 116: Evaluation: Methodology Overview
Evaluation Setup
  CPU: Intel Skylake CPU
  GPU: NVIDIA A100 GPU
  PUD: SIMDRAM [Oliveira+, 2021] and DRISA [Li+, 2017]
  PND: Fulcrum [Lenjani+, 2020]
  https://github.com/CMU-SAFARI/MIMDRAM
Workloads:
  12 workloads from Polybench, Rodinia, Phoenix, and SPEC2017
  495 multi-programmed application mixes
Two-Level Analysis
  Single application → leverages intra-application data parallelism
  Multi-programmed workload → leverages inter-application data parallelism
Notes: We compared MIMDRAM to a high-end CPU and GPU, two state-of-the-art PUD systems that use large DRAM access for computation, and a processing-near-DRAM architecture.
[CLICK] In our analyses, we use 12 workloads from four benchmark suites and 495 application mixes from such workloads
[CLICK] We perform a two-level analysis. For single applications, MIMDRAM can leverage its intra-application data parallelism and for multiple applications, MIMDRAM leverages inter-application data parallelism
[NEXT]

## Slide 117: Evaluation: Single Application Analysis – Energy Efficiency
MIMDRAM significantly improves energy efficiency compared to CPU (30.6x), GPU (6.8x), and SIMDRAM (14.3x)
Takeaway
Chart: CPU-Normalized Performance/Watt
| 2mm | 3mm | cov | doitgen | fdtd | gemm | gs | hw | kmeans | bp | pca | x264 | GMean
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 0.134 | 0.138 | 0.036 | 0.063 | 0.163 | 0.012 | 0.009 | 0.015 | 0.04271
SIMDRAM | 2.346 | 2.328 | 8.195 | 0.343 | 2.626 | 2.35 | 2.994 | 0.041 | 5.189 | 62.814 | 0.153 | 15.696 | 2.1379
MIMDRAM | 30.754 | 36.108 | 199.081 | 13.408 | 2.689 | 26.765 | 35.272 | 1.429 | 123.361 | 2397.384 | 2.294 | 92.782 | 30.6103
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 118: Evaluation: More in the Paper
MIMDRAM with subarray and bank-level parallelism
  MIMDRAM provides significant performance gains compared to the baseline CPU (13.2x) and GPU (2x)
Comparison to DRISA and Fulcrum for multi-programmed workloads
  MIMDRAM achieves system throughput on par with DRISA and Fulcrum
MIMDRAM’s SIMD utilization versus SIMDRAM
  MIMDRAM provides 15.6x the utilization of SIMDRAM
Area analysis
  MIMDRAM adds small area cost to a DRAM chip (1.11%) and CPU die (0.6%)
Notes: We have many more results in our paper, including.
[CLICK] Comparison to DRISA and Fulcrum for multi-applications
[CLICK] SIMDRAM utilization versus SIMDRAM
[CLICK] MIMDRAM’s performance with subarray and bank-level parallelism
[CLICK] and area analysis
[NEXT]

## Slide 119: Evaluation: More in the Paper
MIMDRAM with subarray and bank-level parallelism
  MIMDRAM provides significant performance gains compared to the baseline CPU (13.2x) and GPU (2x)
Comparison to DRISA and Fulcrum for multi-programmed workloads
  MIMDRAM achieves system throughput on par with DRISA and Fulcrum
MIMDRAM’s SIMD utilization versus SIMDRAM
  MIMDRAM provides 15.6x the utilization of SIMDRAM
Area analysis
  MIMDRAM adds small area cost to a DRAM chip (1.11%) and CPU die (0.6%)
https://arxiv.org/pdf/2402.19080.pdf
https://github.com/CMU-SAFARI/MIMDRAM
Notes: For all that, I invite you to check our paper
[NEXT]

## Slide 120: Processing-in-Memory: Challenges
  To fully support PIM systems, we need to develop:
1
Workload characterization methodologies and benchmark suites targeting PIM architectures
2
Frameworks that can facilitate the implementation of complex operations and algorithms using PIM primitives
3
Compiler support and compiler optimizations targeting PIM architectures
4
Operating system support for PIM-aware virtual memory, memory management, data allocation and mapping
5
Efficient data coherence and consistency mechanisms
  The lack of tools and system support for PIM architectures limit the adoption of PIM system

## Slide 121
https://www.youtube.com/onurmutlulectures
Processing-in-Memory Course: Fall 2024
Fall 2024 Edition
  https://safari.ethz.ch/projects_and_seminars/fall2024/doku.php?id=processing_in_memory
Spring 2023 Edition
  https://safari.ethz.ch/projects_and_seminars/spring2023/doku.php?id=processing_in_memory
YouTube Livestream
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi9DSQg7OAlsNO8dOQKxF9sl
Bachelor’s Course:
  Elective at ETH Zurich
  Introduction to PIM systems (from industry and academia)
  Tutorial on using real PIM infrastructure
  Potential research exploration

## Slide 122
PIM Tutorial: ISCA & MICRO 2024
ISCA 2024 Edition
  June 29th: Lectures, hands-on labs, and invited lectures
  https://events.safari.ethz.ch/isca24-memorycentric-tutorial/doku.php?id=start
MICRO 2024 Edition (Upcoming)
  November 2nd: Lectures, hands-on labs, and invited lectures
  https://events.safari.ethz.ch/micro24-memorycentric-tutorial/doku.php?id=start
YouTube Livestream
  https://www.youtube.com/watch?v=KV2MXvcBgb0

## Slide 123
Next PIM Tutorial: PPoPP 2025
https://events.safari.ethz.ch/ppopp25-memorycentric-tutorial/doku.php

## Slide 124
1st Memory-Centric Computing Systems Workshop @ ASPLOS 2025
https://events.safari.ethz.ch/asplos25-MCCSys/doku.php

## Slide 125: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 126: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 127: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, 2023
https://arxiv.org/pdf/1903.03988.pdf
Notes: And check our book chapter on PIM research.
[NEXT]

## Slide 128: Enabling the Adoption of Data-Centric Systems: Hardware/Software Support for Processing-Using-Memory Architectures
Geraldo F. Oliveira geraldofojunior@gmail.com
https://geraldofojunior.github.io/
Memory & Storage Summit 2024 − 07 December 2024
Notes: Hi, I’m Geraldo, a PhD Student under the supervision of professor Multu at ETH Zurich and I’ll be talking about our work DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks.
[NEXT]